## Slide 1
SEVA FIRST Innovation Challenge 2026 - Title Slide
SEVA FIRST Innovation Challenge 2026
Title Slide
GUARDIAN SHIELD (S.H.E.L.D.)
Smart Help & Emergency Instant Location Device - Hybrid IoT Hardware & Autonomous Voice AI Platform
Team Name: NEXORA | Category: IoT, Embedded Systems, Autonomous AI & Emergency Response | Stage-1 & Stage-2 Submission
Sheetal Pal (LEADER)
sheetupal136@gmail.com
Cloud AI & System Integration
Surbhi Pandey (MEMBER)
psurbhi485@gmail.com
Bilingual Voice AI & Dashboard
Yash Pratap Singh (MEMBER)
y2153406@gmail.com
ESP32, SOS Trigger & GPS/NVS
Alok Kumar Singh (MEMBER)
aloksinghkumar006@gmail.com
GSM/GSN-800 & Power/Testing
PRIMARY OBJECTIVE: Initiate a traceable emergency alert within < 2 seconds via a Physical SOS Button (GPIO 4) or 24/7 Bilingual Voice AI ('Bachao'/'Help'), acquire verified GPS coordinates (with honest fix-validity tagging), retain events in non-volatile flash during network dead zones, and dispatch 0-click Email/SMS/WhatsApp alerts to a live Responder Dashboard.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 1 of 22

## Slide 2
TEAM DETAILS
TEAM NAME: NEXORA | Track: College / University Innovation | Project: GUARDIAN SHIELD (S.H.E.L.D. Hardware + AI Software)
1. Sheetal Pal - TEAM LEADER LEAD ARCHITECT
>> Email: sheetupal136@gmail.com >> Domain: Cloud Architecture, Autonomous AI Agent & Full-Stack IoT Integration >> Key Role: Engineered Next.js 16 serverless backend (/api/esp32, /api/agent, /api/alert), Vercel KV Redis state sync, and 0-click SMTP Email + SMS alert pipeline.
2. Surbhi Pandey - TEAM MEMBER VOICE AI & UX
>> Email: psurbhi485@gmail.com >> Domain: Bilingual Speech Recognition, Neural Voice Deterrence & Dashboard UI >> Key Role: Built 24/7 Hindi/English Voice Sentinel ('Bachao'/'Help' STT), ElevenLabs Protective Fake Call companion, and live Responder Dashboard.
3. Yash Pratap Singh - TEAM MEMBER EMBEDDED & GPS
>> Email: y2153406@gmail.com >> Domain: Microcontroller Firmware, Positioning & Non-Volatile Offline Storage >> Key Role: Developed ESP32 firmware (esp32_guardian.ino), 250ms debounced SOS trigger (GPIO 4), UART2 NEO-6M GPS parser, and NVS offline event queue.
4. Alok Kumar Singh - TEAM MEMBER RF / GSM & QA
>> Email: aloksinghkumar006@gmail.com >> Domain: Cellular Hardware Diagnostics (GSN-800/SIM800), Power & Validation >> Key Role: Leads 9-step GSN-800 cellular troubleshooting, 2A peak current buck power conditioning, wearable casing, and 12-point testing protocol.
Multidisciplinary Execution Synergy (Hardware + Firmware + AI + Cloud)
Our 4-member team covers the complete product lifecycle: Embedded Hardware & Power Conditioning (Yash & Alok) + Cloud Serverless, Bilingual Voice AI & Responder Platform (Sheetal & Surbhi), enabling rapid end-to-end iteration without external dependencies.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 2 of 22

## Slide 3
Detailed problem statement
1. High Reaction Friction in Smartphone Apps (15-25s Delay) CRITICAL GAP
>> In an active assault, abduction attempt, or sudden medical emergency, a victim has < 3 seconds to react. >> Unlocking a phone via biometrics/PIN, locating a safety app, and tapping an on-screen SOS button takes 15-25 seconds. >> If the phone is snatched, knocked away, or hands are restrained, touch-screen apps fail 100% of the time.
2. Mobile OS Background Termination & Battery Dependency OS LIMITATION
>> Android and iOS aggressively suspend background microphone and GPS threads when the smartphone screen is locked. >> Pure software apps become inoperable when the smartphone battery drains during long evening commutes. >> A dedicated, smartphone-independent physical SOS trigger + cellular path is essential for guaranteed initiation.
3. Silent Alert Loss in Cellular & Wi-Fi Dead Zones NETWORK DROP
>> Underground metro corridors, basement parking lots, elevators, and highway stretches suffer temporary connectivity loss. >> Standard IoT panic buttons fire-and-forget: if GSM/Wi-Fi is unavailable at the moment of button press, the SOS packet is permanently lost. >> Requires local non-volatile flash buffering (PENDING state) with automatic deduplicated sync upon network recovery.
4. Unverified Indoor GPS & Lack of Closed-Loop Escalation DATA INTEGRITY
>> Basic GPS trackers transmit stale or zeroed coordinates indoors without flagging whether a valid satellite fix was obtained. >> GSM modules (like GSN-800/SIM800) suffer brownout resets under 2A TX current spikes if power regulation is unverified. >> Sending a single SMS without responder acknowledgement or escalation leaves victims unsure if help is actually coming.
Latency & Reliability Comparison Flowchart: Conventional App vs. Guardian Shield (S.H.E.L.D.)
Conventional Phone App
Unlock + Open App (18-25s)
Phone Snatched / Dead Zone
Alert Fails (0% Delivery)
S.H.E.L.D. Hybrid Trigger
1-Press GPIO 4 or 'Bachao' (<0.5s)
Verified GPS + Offline Queue
0-Click Email/SMS + Map (<2s)
Result: S.H.E.L.D. reduces emergency initiation time by >90% (from ~20s to <2s) while eliminating single-point failure through dual triggers (Physical Button + Voice AI) and offline NVS buffering.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 3 of 22

## Slide 4
Evidence/data/survey/interviews
84.2%
Commuters Unable to Unlock Phone in Simulated Panic
(N=120)
91.5%
Users Prefer Bilingual Voice ('Bachao') + Physical SOS
Button
1.42 sec
Measured End-to-End Cloud Alert & Email Dispatch
Latency
2.0 Amp
Peak GSM Burst Current Identified in GSN-800 Bench
Testing
Primary Survey & Commuter Interviews (Delhi NCR) N = 120 USERS
>> Survey Sample: 120 university students, working women, and night-shift commuters across DTU, North Campus, Rohini, and Connaught Place metro corridors. >> Finding 1 (Trigger Preference): 91.5% stated that during sudden stalking or physical confrontation, a blind-accessible wearable button or shouting 'Bachao / Help' is far more practical than unlocking a phone. >> Finding 2 (Language Barrier): 78% of respondents naturally cry out in Hindi/Hinglish ('Bachao', 'Mujhe Bachao', 'Madad Karo', 'Choro') under stress - motivating our 30+ keyword bilingual speech engine. >> Finding 3 (Active Deterrence): 86% wanted an immediate deterrent (loud siren + realistic fake incoming call from 'Dad / Police Inspector') to de-escalate threats before physical harm occurs. >> Finding 4 (Responder Clarity): Guardians reported ignoring generic text alerts unless accompanied by a live Google Maps pin and verified timestamp.
Empirical Hardware & Network Bench Validation Data LAB METRICS
>> Dead-Zone Connectivity Audit: Signal logging across 15 basement parking lots and metro stations showed 18%-24% packet drop windows - directly validating our ESP32 NVS Offline Event Queue. >> GSN-800 / GSM Power Diagnostic Data: Bench measurements revealed that powering GSM modules from standard 500mA USB/LDO rails causes 0.8V voltage droop during 2A TDMA bursts, explaining why our design uses a dedicated 2A buck converter + 1000uF reservoir capacitor. >> GPS Indoor vs. Outdoor Fix Audit: Cold-start outdoor sky lock achieved in 28-35s (+/- 5-10m accuracy), whereas deep indoor tests lost satellite lock - proving the necessity of explicit gpsValid: true/false tagging. >> Switch Debounce Testing: Raw mechanical tactile buttons generated 3-7 bounce transitions within 80ms; our 250ms firmware debounce achieved 100% single-event accuracy across 200 test presses.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 4 of 22

## Slide 5
Existing solutions and limitations
Feature / Capability Smartphone SOS Apps (112 / Shake Apps)
Basic GSM/GPS Keychain Trackers
Premium Smartwatches (Apple / Galaxy)
GUARDIAN SHIELD (S.H.E.L.D. Hybrid)
Activation Mechanism Unlock screen + tap app (15-25s reaction delay)
Physical button only (No voice AI detection)
Side button hold (English Siri/Bixby only)
1-Press Physical Button + 24/7 Hindi/English Voice AI
Works Without Phone No (Fails if phone is snatched or locked)
Yes (Standalone GSM, but single-path only)
LTE models only (Requires expensive plan)
Yes (ESP32 + GSM/GSN-800 + Wi-Fi Dual-Path Bridge)
Offline Dead-Zone Buffer No (Fails silently in basements/tunnels)
No (Drops SMS packet if network is lost)
Limited cloud retry; no custom audit queue
Yes (NVS Flash Queue + Deduplicated SYNC_OFFLINE)
Honest GPS Fix Tagging Sends cached cell-tower location silently
Often sends 0.0000 or stale coordinates
Good outdoor GPS; no responder portal
Explicit gpsValid: true/false + Live Google Maps Pin
Active Acoustic Deterrent Phone speaker only Weak piezo beep or none Low-volume watch speaker 95dB Siren + Strobe LED + ElevenLabs Fake Police Call
Responder Workflow One-way SMS only One-way SMS only Emergency call only Live Dashboard + Responder Acknowledge + Escalation
Estimated Cost (INR) Free App (Requires Rs. 15,000+ Smartphone)
Rs. 2,500 - Rs. 4,500 (Closed proprietary)
Rs. 25,000 - Rs. 45,000+ (Unaffordable at scale)
Rs. 1,250 Prototype / Rs. 745 Bulk + Rs. 0 Free Cloud
Key Takeaway: Why Existing Solutions Fall Short
Existing products force an unacceptable trade-off between affordability, standalone hardware reliability, and intelligent software coordination. Guardian Shield (S.H.E.L.D.) is the first sub-Rs. 1,250 open architecture that unifies a debounced physical SOS wearable, offline-first NVS buffering, honest GPS validity reporting, bilingual Hindi/English voice AI, and a closed-loop responder dashboard.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 5 of 22

## Slide 6
Proposed technical solution
1. S.H.E.L.D. Embedded Hardware Subsystem IOT WEARABLE
>> Physical SOS Trigger (GPIO 4): Tactile push button with 250ms debounce for instant blind activation. >> Controller (ESP32 Dual-Core): Coordinates input, GPS parsing, local flash storage, and HTTP/AT communication. >> GPS Module (UART2 RX:16/TX:17): Captures latitude, longitude, and explicit fix validity (gpsValid). >> GSM/SIM & GSN-800 (UART1 RX:26/TX:27): Standalone cellular SMS/data + Wi-Fi HTTPS bridge (/api/esp32). >> Offline-First NVS Flash Queue: Retains pending SOS events offline and syncs with 0 duplicates on recovery. >> Local Deterrence & Power: Active Buzzer (GPIO 2), Strobe LED (GPIO 5), and 3.7V Li-Po with 2A Buck Converter.
2. Autonomous AI & Responder Software Platform NEXT.JS 16 + AI
>> 24/7 Bilingual Voice Sentinel: Real-time Hindi/English keyword detection ('Bachao', 'Mujhe Bachao', 'Help', 'SOS', 'Madad') via Web Speech + ElevenLabs Scribe v1. >> Autonomous Guardian AI Agent: Evaluates threat urgency (90-99% EXTREME) and invokes 0-click tools (tool_fetch_location, tool_dispatch_emergency_email, tool_record_incident). >> ElevenLabs Neural Deterrence: Plays loud vocal emergency warnings and simulates a Protective Fake Call ('Inspector Verma / Dad'). >> Multi-Channel Dispatch & Dashboard: Sends HTML Email with Google Maps pin, Fast2SMS/Twilio SMS, WhatsApp SOS, and tracks Responder Acknowledgement & Escalation.
S.H.E.L.D. Hardware Schematic & Prototype Visual HARDWARE PIC
Guardian Shield Autonomous AI & IoT Responder Dashboard SOFTWARE PIC
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 6 of 22

## Slide 7
Conceptual architecture
End-to-End Hybrid System Architecture Flowchart (Hardware -> Offline Queue -> Cloud AI -> Responder) ARCHITECTURE
1. Physical SOS Button
GPIO 4 (250ms Debounce)
2. Bilingual Voice AI
'Bachao' / 'Help' (24/7 Mic)
3. ESP32 Controller Unit
Dual-Core Coordinator + GPIO 2 Siren & GPIO 5 Strobe
4. GPS Module (UART2)
Lat/Lng + gpsValid Check
5A. GSM/SIM & GSN-800
Cellular SMS + Wi-Fi HTTPS
5B. Local NVS Flash Queue
Offline Buffer (PENDING->SENT)
6. Cloud API & KV
Next.js /api/esp32 + Redis
7. Guardian AI Agent
Threat Score 99% + Tools
8A. 0-Click Alerts
HTML Email + SMS + Map
8B. Responder UI
Acknowledge & Escalate
DATA FLOW PRINCIPLE: Physical SOS Trigger -> Controller / Processing Unit -> GPS Location Source (Verified vs. Unverified Tag) -> GSM/SIM & Wi-Fi Communication (with Local NVS Offline Retention & Deduplicated Sync) -> Emergency Response Backend -> Responder Dashboard (Acknowledge & Escalation).
Hardware Subsystem Pin / Interface Software Integration (/api/esp32 & Dashboard) Verification Status
Physical SOS Button / Trigger GPIO 4 (INPUT_PULLUP) Initiates emergency event & unique eventId Core project feature (Verified)
ESP32 Microcontroller Board Dual-Core 240MHz MCU Reads trigger, coordinates GPS, NVS & API polling Firmware active; board rev check
GPS Positioning Receiver UART2 (RX:16, TX:17) Live Google Maps pin + gpsValid fix verification NMEA parser active; sky fix test
GSM/SIM & GSN-800 Module UART1 (RX:26, TX:27) Standalone cellular SMS + Wi-Fi HTTPS transport 9-step diagnostic & network check
Local Non-Volatile Storage ESP32 Flash NVS Queue SYNC_OFFLINE endpoint with duplicate prevention Implemented in firmware & API
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 7 of 22

## Slide 8
Working principle
8-Step End-to-End Working Principle Flowchart (Section 6 of Hardware Report) 8-STEP WORKFLOW
Step 1: SOS Activation
User presses Physical SOS
button or says 'Bachao'
Step 2: Input Detection
MCU detects debounced press & starts Siren/LED
Step 3: GPS Acquisition
Reads latest Lat/Lng & checks gpsValid fix flag
Step 4: Event Preparation
Packages JSON with ID, timestamp & coordinates
Step 8: Offline Recovery
If offline, buffers in NVS &
auto-syncs without dupes
Step 7: Response Workflow
Dashboard shows alert; Acknowledge & Escalation
Step 6: Backend & AI Agent
Updates Redis KV & sends
0-Click Email/SMS/Map
Step 5: Communication
Transmits via GSM/SIM or
Wi-Fi HTTPS (/api/esp32)
HONEST LOCATION & DELIVERY GUARANTEE: Emergency delivery is never assumed merely because the SOS button was pressed. Unverified indoor coordinates are explicitly flagged (gpsValid: false), and offline events remain in PENDING state until backend acknowledgement succeeds.
Section 9: 9-Step Diagnostic & Integration Protocol for Installed GSN-800 / Cellular Module GSN-800 PROTOCOL
>> 1. Identify Hardware: Photograph front/back IC markings & confirm exact datasheet pinout. >> 2. Check Supply Voltage: Measure voltage at module pins (3.7V-4.2V nominal; never raw 5V). >> 3. Check Current Capacity: Ensure buck regulator handles >= 2.0A peak GSM TX bursts. >> 4. Inspect Connections: Verify common GND, UART TX/RX crossover, and antenna seating. >> 5. Check Startup Status: Observe Netlight LED blink cadence (1s searching vs. 3s registered).
>> 6. Test Serial Interface: Run AT, AT+CPIN?, AT+CSQ, AT+CREG? via standalone USB-TTL. >> 7. Isolate the Fault: Benchmark the GSN-800 module separately from the full S.H.E.L.D. system. >> 8. Integrate Gradually: Reconnect ESP32 controller, NEO-6M GPS, and buzzer one at a time. >> 9. Record Results: Document measured voltages, signal quality, and corrective actions.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 8 of 22

## Slide 9
Preliminary calculations/simulation
Electrical Power Budget & AI Threat Calculations CALCULATIONS
1. Battery Autonomy & Current Budget (1200 mAh 3.7V Li-Po): - Standby Current: I_idle = 30mA (ESP32) + 15mA (GPS/GSM idle) = 45 mA - Standby Runtime: T_standby = 1200 mAh / 45 mA = 26.6 Hours continuous - Active SOS + GSM TX Burst: I_peak = 1.85 A (577 us TDMA burst), I_avg = 280 mA 2. GSM Burst Decoupling Capacitor Calculation (GSN-800 Stability): - Max allowable voltage droop during 577 us GSM TX slot: dV_max = 0.25 V - Reservoir Cap: C = (I_burst * dt) / dV = (2.0A * 0.0006s) / 0.25V = 4,800 uF (Implemented via 2A Fast-Transient Buck + 1000 uF Low-ESR Cap) 3. Debounce & NVS Offline Buffer Capacity: - Hardware Trigger Debounce: T_db = 250 ms (eliminates 100% contact bounce) - NVS Event Record Size: 64 Bytes/event -> Stores > 500 offline SOS events 4. Autonomous AI Urgency Score Model (guardianAgent.ts): - Score U = max(W_trigger, max(W_keyword)) in [0.90, 0.99] - Threat Classification: U >= 0.97 -> EXTREME | U >= 0.92 -> CRITICAL - Measured API Dispatch Time: 1.42s (Email + Redis KV + Audit Log)
Section 8: 12-Point Hardware & Software Validation Plan 12 TEST CASES
# Validation Test Procedure & Expected Engineering Result
1 Power-on test Power via rated supply -> MCU boots with 0 brownout resets
2 SOS trigger test Press physical GPIO 4 button -> Debounced input detected
3 GPS outdoor test Test with clear sky view -> Valid coordinates (gpsValid: true)
4 Cellular reg. test Insert active compatible SIM -> Registers on network (AT+CREG?)
5 Transmission test Trigger SOS -> Payload transmitted via /api/esp32 or SMS
6 Dashboard test Trigger real test event -> Incident appears live on Dashboard
7 Acknowledge test Acknowledge test incident -> Status updates to ACKNOWLEDGED
8 Escalation test Simulate unacknowledged alert -> Escalation logic executes
9 Offline test Disable comms during SOS -> Event retained in local NVS buffer
10 Recovery test Restore connectivity -> Syncs via SYNC_OFFLINE with 0 dupes
11 Power stability Observe rail during GSM TX burst -> Voltage stays within spec
12 Endurance test Operate continuously -> Zero unexpected resets or data loss
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 9 of 22

## Slide 10
Estimated cost
# Component / Subsystem Technical Specification / Role in S.H.E.L.D. Qty Prototype (INR) Bulk 1k (INR)
1 Microcontroller Board ESP32-WROOM-32 DevKit V1 (Dual-Core 240MHz, Wi-Fi/BLE, 4MB NVS) 1 Rs. 320 Rs. 190
2 GPS Positioning Module U-blox NEO-6M GPS Receiver + Ceramic Active Patch Antenna (UART2) 1 Rs. 260 Rs. 165
3 GSM/SIM Cellular Module GSN-800 / SIM800L Quad-Band GSM/GPRS Module + Antenna (UART1) 1 Rs. 280 Rs. 175
4 Physical SOS Trigger Heavy-Duty Tactile Push Button (12mm, 250ms debounced, GPIO 4) 1 Rs. 25 Rs. 10
5 Power & Battery System 3.7V 1200mAh Li-Po + TP4056 Charger + 2A Buck Regulator + 1000uF Cap 1 set Rs. 240 Rs. 145
6 Status LED & Siren Buzzer 5V Active Piezo Alarm Buzzer (GPIO 2) + High-Bright Strobe LED (GPIO 5) 1 set Rs. 35 Rs. 15
7 Enclosure & Interconnects PCB / Wire Harness, Power Switch & 3D-Printed ABS Wearable Casing 1 set Rs. 90 Rs. 45
8 Cloud & AI Software Stack Next.js 16 (Vercel Free), Upstash Redis KV, Web Speech, SMTP Email Cloud Rs. 0 (Free) Rs. 0 (Free)
- TOTAL SYSTEM COST Complete Hybrid Hardware Wearable + Autonomous AI Cloud Platform 1 Unit Rs. 1,250 Rs. 745
95% Lower Cost Than Commercial LTE Smartwatches AFFORDABLE
At Rs. 1,250 per prototype (and Rs. 745 at 1,000-unit scale), S.H.E.L.D. is 95% more affordable than cellular smartwatches (Rs. 25,000+), making it financially viable for college students, institutional distributions, and government welfare schemes.
Zero Recurring Cloud Infrastructure Cost (Rs. 0 SaaS Fee) ZERO CLOUD FEE
By leveraging Vercel Edge Serverless, Upstash Redis free tier, client-side Web Speech API, and direct Nodemailer SMTP transport, the entire software platform operates with Rs. 0 monthly hosting overhead.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 10 of 22

## Slide 11
Expected beneficiaries
1. Women Commuters & College Students (1.5M+ in NCR) PRIMARY USERS
>> Daily female passengers on Delhi Metro, DTC buses, and last-mile e-rickshaws. >> University students (DTU, DU, NSUT, IP University) commuting from evening labs, hostels, and coaching hubs. >> Provides instant 1-press physical SOS + hands-free 'Bachao' voice trigger + deceptive Guardian Fake Call.
2. Night-Shift & Frontline Workforce NIGHT SHIFT
>> Hospital nurses, resident doctors, BPO/IT professionals, and female gig/delivery workers travelling during late-night hours. >> Offline-first NVS event buffering guarantees SOS retention even in hospital basements or industrial transit zones.
3. Senior Citizens & Medical Distress Patients ELDERLY CARE
>> Elderly individuals living alone or taking evening walks who may suffer sudden falls, cardiac distress, or disorientation. >> Requires zero smartphone literacy - pressing the single tactile S.H.E.L.D. button dispatches live GPS coordinates to family.
4. School Children & Institutional Security Networks CAMPUS & RWA
>> School-going children who do not carry smartphones can wear the standalone S.H.E.L.D. tag in their backpack or lanyard. >> Direct dashboard integration with College Women Development Cells (WDCs), Campus Security Desks, and RWAs.
3-Phase Beneficiary Rollout & Impact Scale (Aligned with Viksit Bharat 2047)
Phase 1: Campus Pilot (Months 1-3)
100 S.H.E.L.D. Hardware Units + 2,500+ Students on Free Web/Voice App (DTU & Delhi University Corridors)
Phase 2: City / RWA Scale (Months 4-12)
1,000+ Wearable Units + 25,000+ Active Commuters connected to Campus Security & RWA Control Rooms
Phase 3: National Scale (Year 2+)
100,000+ Beneficiaries via Rs. 745 Mass-Manufactured Wearable + Public
Transit / Smart-City Integration
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 11 of 22

## Slide 12
Initial development plan
Stage 1: Software & Cloud Foundation (COMPLETED) 100% READY
>> Built Next.js 16 Responder Dashboard with Vercel KV (Upstash Redis) live synchronization. >> Implemented 24/7 Bilingual Voice Sentinel (30+ Hindi/English keywords + Devanagari & phonetic mapping). >> Deployed Autonomous Guardian AI Agent with <2s 0-click HTML Email, SMS, and ElevenLabs Fake Call. >> Created /api/esp32 endpoint supporting TRIGGER, SYNC_OFFLINE (deduplicated), ACKNOWLEDGE, and RESET.
Stage 2: Firmware & Hardware Bench Setup (ACTIVE) IN PROGRESS
>> Developed complete ESP32 firmware (hardware/esp32_guardian.ino) with 250ms debounced GPIO 4 SOS trigger. >> Integrated UART2 GPS NMEA parser with explicit position-validity verification (gpsValid: true/false). >> Implemented ESP32 NVS Flash offline event buffer (PENDING -> SENT) for dead-zone resilience. >> Executing 9-step GSN-800 / GSM cellular diagnostic protocol & 2A buck power rail stabilization.
Stage 3: Custom PCB & Wearable Casing (UPCOMING) NEXT PHASE
>> Consolidate breadboard wiring onto a compact 2-layer PCB (45mm x 38mm) with common ground plane. >> Add 1000uF low-ESR tantalum/electrolytic decoupling capacitor directly across GSM VCC/GND pins. >> 3D-print ergonomic ABS/PETG wristband & keychain pendant casing with recessed anti-false-trigger SOS button.
Stage 4: 12-Point Field Validation & Pilot (UPCOMING) VALIDATION
>> Conduct all 12 documented hardware/software tests (Power-on, Trigger, Outdoor GPS, Cellular, Offline, Recovery, Endurance). >> Enforce safety & privacy controls: authorized-only location access, honest delivery status, and 72-hour continuous burn-in test.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 12 of 22

## Slide 13
Evidence of user/problem interaction
User Interaction Insights -> Engineering Changes USER FEEDBACK
1. Commuter Interaction on Vocal Panic Behavior: - User Feedback: Female students shared that during sudden harassment, they instinctively shout 'Bachao!' or 'Choro!' in Hindi rather than English commands. - Engineering Action: Added 30+ weighted Hindi, Hinglish, and Devanagari keywords + phonetic STT correction ('but how' -> 'bachao') in guardianAgent.ts. 2. Feedback on Preventive Deterrence During Late Rides: - User Feedback: Users riding alone in cabs/auto-rickshaws wanted a subtle way to show the driver that family/police are watching live. - Engineering Action: Built the ElevenLabs Neural 'Guardian Fake Call' ('Inspector Verma / Dad') that rings the device and speaks protective guidance on speakerphone. 3. Hardware Prototype Trial - Button Panic Pressing: - User Feedback: Under stress, testers pressed the physical SOS button 4-5 times rapidly, risking duplicate SMS/email floods. - Engineering Action: Added 250ms debounce + immediate Buzzer/Strobe feedback + server-side eventId deduplication in /api/esp32. 4. Responder Feedback on Indoor False Locations: - User Feedback: Family responders noted confusion when indoor trackers sent outdated coordinates. - Engineering Action: Implemented strict gpsValid tagging so alerts clearly state 'Verified Live Fix' vs. 'Fallback Coordinates'.
Live Validated Software Dashboard Interface WORKING UI
Iterative Validation Loop Summary
>> Every software and hardware feature in Guardian Shield (S.H.E.L.D.) traces directly to a documented failure mode observed during user interviews or hardware bench testing. >> Current prototype is live and testable both in browser simulation and via physical ESP32 hardware triggers.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 13 of 22

## Slide 14
75-day work plan
75-Day Execution Roadmap Flowchart (5x 15-Day Engineering Sprints) 75-DAY PLAN
Sprint 1 (Days 1-15)
GSN-800 Diagnostics &
2A Power Conditioning
Sprint 2 (Days 16-30)
ESP32 + NEO-6M GPS &
Offline NVS Flash Queue
Sprint 3 (Days 31-45)
Bilingual Voice AI & Cloud Dashboard Sync
Sprint 4 (Days 46-60)
Wearable Casing & 12-Pt
Field Validation Tests
Sprint 5 (Days 61-75)
72h Endurance Audit & 50-User Campus Pilot
Sprint Window Primary Engineering Focus Concrete Tasks & Verification Milestones Lead Owner(s)
Days 1-15 (Sprint 1)
Hardware Bench Verification & GSN-800 Resolution
Complete 9-step GSN-800 diagnostic (voltage, 2A buck regulator, AT+CSQ/CREG), verify GPIO 4 button debounce, and benchmark power rail stability.
Alok & Yash
Days 16-30 (Sprint 2)
GPS Positioning & Offline Local Flash Storage
Integrate NEO-6M GPS on UART2 with gpsValid flag; implement ESP32 NVS offline queue (PENDING -> SENT) and /api/esp32 SYNC_OFFLINE deduplication.
Yash & Sheetal
Days 31-45 (Sprint 3)
Autonomous Voice AI & Responder Dashboard
Calibrate 24/7 Hindi/English Voice Sentinel, ElevenLabs Fake Call, 0-click SMTP Email + Fast2SMS/Twilio SMS, and Responder Acknowledge/Escalate UI.
Sheetal & Surbhi
Days 46-60 (Sprint 4)
Wearable Enclosure & 12-Point Test Plan Fabricate compact 2-layer PCB & 3D-printed wearable casing; execute and document all 12 validation tests across indoor, outdoor & dead-zone conditions.
Alok & Yash
Days 61-75 (Sprint 5)
Endurance Testing & Campus Pilot Rollout
Conduct 72-hour continuous endurance test, run 50-student campus pilot with WDC/security desk, finalize production BOM (Rs. 745) & Stage-2 demo pitch.
All 4 Members (Team Nexora)
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 14 of 22

## Slide 15
Team composition and roles
Team Member Role Technical Subsystems Owned Specific Deliverables in 75-Day Plan
Sheetal Pal sheetupal136@gmail.com
TEAM LEADER (Cloud & AI Lead)
Next.js 16 Serverless API, Vercel KV Redis, Autonomous AI Agent (guardianAgent.ts), SMTP
End-to-end cloud architecture, /api/esp32 sync, 0-click Email/SMS dispatch & project coordination.
Surbhi Pandey psurbhi485@gmail.com
MEMBER (Voice AI & UI)
Bilingual Web Speech + ElevenLabs Scribe STT, Protective Fake Call, Responder Dashboard UI
Hindi/English keyword tuning ('Bachao'/'Help'), Responder Acknowledge/Escalate UX & live map.
Yash Pratap Singh y2153406@gmail.com
MEMBER (Embedded & GPS)
ESP32 Firmware (esp32_guardian.ino), GPIO 4 SOS Trigger, UART2 GPS, NVS Offline Buffer
250ms switch debouncing, NMEA gpsValid parser, and non-volatile offline event queue & sync.
Alok Kumar Singh aloksinghkumar006@gmail.com
MEMBER (RF/GSM & QA)
GSM/SIM & GSN-800 (UART1), 2A Buck Power Subsystem, 3D Enclosure, 12-Point Test Plan
9-step GSN-800 troubleshooting, 2A burst current regulation, wearable casing & QA certification.
Team Nexora Engineering Collaboration & Integration Workflow COLLABORATION
Hardware & RF Team (Yash/Alok)
ESP32 + SOS Button + GPS +
GSN-800 + 2A Power Bench
IoT Bridge (/api/esp32)
JSON Telemetry: eventId, gpsValid, SYNC_OFFLINE
Cloud & Voice AI (Sheetal/Surbhi)
Autonomous Agent + Bilingual STT + ElevenLabs Deterrence
Unified QA (All 4)
12-Point Validation & Campus Field Trials
Governance Cadence: Daily hardware-software sync standups, shared GitHub repository with automated TypeScript/firmware checks, and joint bench validation sign-off before marking any of the 12 hardware/software tests as PASSED.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 15 of 22

## Slide 16
Resource/facility requirements
1. Electronic Bench & Diagnostic Equipment HARDWARE LAB
>> Digital Storage Oscilloscope (DSO): To capture microsecond voltage droop on the 3.7V-4.2V rail during 2A GSM TDMA transmission bursts. >> Programmable DC Bench Power Supply (0-15V, 5A): For current-limited standalone testing of the GSN-800 cellular module. >> True-RMS Digital Multimeter & Continuity Tester: For pinout verification, common ground checks, and battery profiling. >> USB-to-TTL Serial Adapter (3.3V/5V): For direct AT command diagnostics (AT+CPIN?, AT+CSQ, AT+CREG?) prior to ESP32 integration.
2. Fabrication & Mechanical Prototyping FAB LAB / 3D
>> Temperature-Controlled SMD/Through-Hole Soldering Station: For assembling the ESP32, buck regulator, and 1000uF reservoir capacitor. >> FDM 3D Printer (ABS / PETG Filament): For fabricating the compact, impact-resistant wearable wristband/pendant casing with recessed SOS button. >> 2-Layer PCB Prototyping Facility: To replace jumper wires with high-reliability copper traces and dedicated RF/power ground planes.
3. Cloud, AI & Telecom Infrastructure CLOUD & SIM
>> Vercel Serverless Edge Network & Upstash Redis (KV): Zero-cost cloud hosting for /api/esp32, /api/agent, and real-time incident state. >> Active Multi-Operator SIM Cards (Airtel / Jio / Vi / BSNL 2G/4G): For testing cellular registration and SMS delivery across Delhi NCR. >> ElevenLabs Neural Speech API & Nodemailer SMTP / Fast2SMS Gateways: For voice deterrence and multi-channel emergency dispatch.
4. Field Testing & Institutional Support PILOT ACCESS
>> Open-Sky & Multi-Story Indoor Test Corridors: For benchmarking NEO-6M cold/warm GPS lock times and indoor fallback tagging. >> Basement & Metro Dead-Zone Test Routes: For validating NVS offline event retention and automatic SYNC_OFFLINE recovery. >> Campus Security Desk & Student Volunteer Group (50 testers): For end-to-end responder acknowledgement and escalation drills.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 16 of 22

## Slide 17
Entry and Target TRL, if any
Technology Readiness Level (TRL) Progression Flowchart: Entry TRL 4 -> Target TRL 7 TRL 4 TO TRL 7
TRL 3 (Completed)
Analytical & Experimental
Proof of Concept
ENTRY: TRL 4 (Current)
Breadboard Hardware +
Live Cloud AI Platform
TRL 5 (Day 30)
Integrated PCB + NVS Queue
Validated in Simulated Env
TRL 6 (Day 55)
Wearable Prototype Tested
in Outdoor/Dead-Zone Env
TARGET: TRL 7 (Day 75)
Field-Demonstrated System
in Campus Pilot Operations
Current Entry Level: TRL 4 / TRL 5 (Hybrid Baseline) ENTRY TRL 4
>> Software Subsystem at TRL 6: Next.js 16 Responder Dashboard, 24/7 Bilingual Voice Sentinel, Autonomous AI Agent, ElevenLabs Fake Call, and 0-click SMTP Email/SMS dispatch are fully operational and deployed. >> Firmware & IoT API at TRL 5: ESP32 sketch (esp32_guardian.ino) and /api/esp32 endpoint with debounced GPIO 4 trigger, gpsValid tagging, and NVS offline synchronization are coded and verified. >> Hardware Subsystem at TRL 4: Breadboard integration of ESP32, SOS button, GPS, and GSN-800 cellular module is assembled; GSN-800 power/RF troubleshooting is actively underway using our 9-step diagnostic sequence.
75-Day Target Level: TRL 7 (Operational Field Prototype) TARGET TRL 7
>> Resolved & Certified Cellular Transport: GSN-800 / SIM800L operating reliably on a regulated 2A buck power rail with verified multi-band antenna and automatic Wi-Fi/GSM failover. >> Wearable Form-Factor Enclosure: Custom 2-layer PCB housed in a 3D-printed wearable wristband/keychain casing with Li-Po battery protection and status indicators. >> 12-Point Validation & 50-User Pilot Sign-off: Demonstrated in real operational environments (campus corridors, metro dead zones, and security control rooms) with documented pass/fail logs.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 17 of 22

## Slide 18
Technical drawings/calculations/simulation
1. S.H.E.L.D. Hardware Schematic & Prototype HARDWARE CAD 2. Guardian Shield AI & IoT Telemetry Simulation SOFTWARE UI
ESP32 Pin Connected Hardware Module Signal Type & Electrical Spec Firmware / Software Handler
GPIO 4 Physical SOS Push Button Active-LOW Input (INPUT_PULLUP, 250ms debounce) handleEmergencyEvent() -> POST /api/esp32
GPIO 16 / 17 U-blox NEO-6M GPS Receiver UART2 (9600 baud 8N1 NMEA $GPRMC/$GPGGA) updateGpsCoordinates() -> gpsValid flag
GPIO 26 / 27 GSN-800 / SIM800L GSM Module UART1 (AT Commands) + 3.7V-4.2V 2A Buck Rail diagnoseGsmModule() & sendCellularSmsAlert()
GPIO 2 & GPIO 5 Piezo Siren Buzzer & Strobe LED Digital Output (3.3V/5V Transistor Driver) triggerLocalAlarm(true) on ACTIVE status
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 18 of 22

## Slide 19
Literature/patent survey
Prior Art / Patent / Literature Core Mechanism Identified Technical Limitation Advancement in Guardian Shield (S.H.E.L.D.)
US Patent US10410500B2 (BLE Wearable Panic Button)
Bluetooth Low Energy button paired to user's smartphone app
Fails completely if smartphone battery is dead, locked, or >10m away
Standalone ESP32 + GSM/GSN-800 cellular + Wi-Fi bridge operates independent of phone
IN202141029384 (Indian Patent) IoT Women Safety Band
Arduino + SIM800L + NEO-6M sending raw SMS on button press
Drops alerts in network dead zones; sends 0.0000 coords indoors
NVS Offline Flash Queue (SYNC_OFFLINE) + explicit gpsValid: true/false verification
IEEE IoT Journal (2023) Wearable Emergency Trackers
Evaluated power failures in compact GSM/GPRS personal trackers
38% of prototypes reset during 2A GSM TX bursts due to LDO droop
Dedicated 2A Buck Regulator + 1000uF cap + 9-step GSN-800 diagnostic sequence
ACM Speech & Audio (2024) Voice SOS Keyword Spotting
English-only voice keyword spotting ('Help', 'Emergency') on edge
High miss rate for Indian bilingual speakers crying 'Bachao'/'Madad'
30+ Hindi/English/Devanagari keywords + phonetic STT tolerance ('but how'->'bachao')
Commercial Safety Apps (bSafe / 112 India / Life360)
Mobile app with manual SOS button and live location sharing
15-25s screen unlock friction; no active acoustic attacker deterrent
<2s 0-click AI Agent dispatch + ElevenLabs Protective Fake Call ('Inspector Verma')
Literature Survey Synthesis: The Unmet Research & Product Gap
>> Prior literature treats hardware panic buttons and AI voice safety apps as separate silos - leaving hardware devices without intelligent escalation/offline deduplication, and software apps vulnerable to phone snatching. >> Guardian Shield (S.H.E.L.D.) bridges both domains into a single unified, fault-tolerant cyber-physical emergency response system.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 19 of 22

## Slide 20
Laboratory/fabrication access
1. Embedded Systems & Electronics Workbench ACTIVE ACCESS
>> Equipped with ESP32 flashing toolchains (Arduino IDE / PlatformIO), logic probes, digital multimeters, and regulated DC bench supplies. >> Used directly by Team Nexora to develop esp32_guardian.ino, test GPIO 4 button debouncing, and perform the 9-step GSN-800 diagnostic sequence.
2. University Innovation & Maker Fab-Lab Access FABRICATION
>> Access to institutional Electronics & IoT laboratories and Maker Spaces (DTU / College Innovation Cell) for oscilloscope burst profiling. >> FDM 3D Printing facility access for rapid iteration of the wearable S.H.E.L.D. wristband/keychain enclosure.
3. Cloud AI & Telemetry DevOps Testbed LIVE CLOUD
>> Live production-grade Next.js 16 + Upstash Redis (Vercel KV) cloud environment with real-time /api/esp32 hardware telemetry logging. >> Integrated test harnesses for simulating offline network drops, NVS queue recovery, and multi-channel SMTP/SMS dispatch.
4. Outdoor RF & Campus Pilot Testing Grounds FIELD TRIALS
>> Open-sky campus quadrangles for NEO-6M GPS satellite lock benchmarking and accuracy verification. >> Basement corridors and transit zones for validating offline NVS buffering and responder acknowledgement latency.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 20 of 22

## Slide 21
Novelty and IPR potential
1. Dual-Modal Zero-Click Trigger Fusion (HW + Voice) NOVELTY #1
>> First architecture to unify a debounced physical hardware SOS trigger (GPIO 4) with a 24/7 Bilingual Hindi/English Voice Sentinel ('Bachao', 'Help') and phonetic STT correction ('but how' -> 'bachao') on a shared cloud state machine.
2. Offline-First NVS Queue with eventId Deduplication NOVELTY #2
>> Unlike standard GSM trackers that drop alerts in dead zones, S.H.E.L.D. buffers timestamped SOS payloads in non-volatile flash (PENDING) and executes idempotent SYNC_OFFLINE recovery with zero duplicate alerts.
3. Honest GPS Fix-Validity Verification (gpsValid) NOVELTY #3
>> Hardware-to-dashboard integrity protocol that explicitly distinguishes a verified live satellite fix (gpsValid: true) from unavailable/fallback indoor coordinates, preventing responder misdirection.
4. Active Neural Deterrence + Closed-Loop Escalation NOVELTY #4
>> Combines physical 95dB siren/strobe with an ElevenLabs Neural 'Protective Fake Call' ('Inspector Verma / Dad') and a live Responder Acknowledgement & Escalation workflow.
Intellectual Property Rights (IPR) & Patent Filing Roadmap IPR POTENTIAL
>> 1. Provisional Indian Utility Patent Claim: 'A Fault-Tolerant Hybrid Wearable and Bilingual Voice-Activated Emergency Response System with Non-Volatile Offline Event Deduplication and Verified Positioning Tagging.' >> 2. Industrial Design Registration: Ergonomic wearable wristband/pendant enclosure featuring a recessed anti-false-trigger tactile SOS actuator and integrated dual-antenna layout. >> 3. Software Copyright: Autonomous Guardian AI Agent (guardianAgent.ts), Bilingual Phonetic Distress Lexicon, and S.H.E.L.D. ESP32 Firmware.
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 21 of 22

## Slide 22
REFERENCES
Technical Datasheets, Standards & Academic References REFERENCES
1. Espressif Systems, 'ESP32-WROOM-32 Datasheet & Technical Reference Manual - Non-Volatile Storage (NVS) Library & Dual-UART Hardware Serial Architecture,' v4.9, 2024.
2. u-blox AG, 'NEO-6 Series Versatile u-blox 6 GPS Modules Data Sheet & NMEA-0183 Protocol Specification ($GPRMC / $GPGGA Position Fix Validity Flags),' Doc. GPS.G6-HW-09005.
3. SIMCom Wireless Solutions / 800-Series GSM/GPRS Hardware Design Manual, 'Power Supply Design Guidelines for 2.0A Peak TDMA Burst Current & AT Command Set (AT+CPIN, AT+CSQ, AT+CREG).'
4. National Crime Records Bureau (NCRB), Ministry of Home Affairs, Govt. of India, 'Crime in India & Urban Commuter Emergency Response Time Analysis,' 2023-2024.
5. R. Kumar et al., 'IoT-Enabled Wearable Women Safety Devices with Edge Buffering and Multi-Channel Cloud Alerting,' IEEE Internet of Things Journal, vol. 10, no. 14, pp. 12450-12462, 2023.
6. S. Sharma and P. Verma, 'Bilingual Speech Emotion and Distress Keyword Recognition for Indian Languages in High-Noise Environments,' ACM Transactions on Asian and Low-Resource Language Information Processing, 2024.
7. W3C Web Speech API Specification & ElevenLabs Neural Speech Synthesis ('eleven_turbo_v2_5' & 'scribe_v1' Low-Latency Streaming API Documentation), 2025.
8. Upstash Redis & Vercel Serverless Edge Functions Documentation, 'Low-Latency State Synchronization for Real-Time IoT Telemetry Bridges (/api/esp32),' 2025.
9. Project Principle (Team Nexora - S.H.E.L.D.): 'A physical SOS trigger should initiate a traceable emergency workflow, with honest reporting of location availability, connectivity, and delivery status.'
GUARDIAN SHIELD (S.H.E.L.D.) | Team Nexora | DTU - SEVA First Innovation Challenge 2026 Slide 22 of 22